The hardware description language is EHDL.
Official documentation.
Documentation to the header file
"esl.h " versions 0.12.1 and above.
Edition №11

An overview of the available functions

Section #1 "Logic gates"

And()
Prototype: int and(usi args [], usi* out);
This function acts as the logical element "And", returns 1 if all elements of args[] are equal to 1, otherwise returns 0. In addition to the values returned by the function, you can get a signal from the output by reading the passed array out, where the result of the function is stored in the last element of the array.

Or()
Prototype: int Or(usi args [], usi* out);
This function acts as a logical element "Or", returns 1 if at least one of the elements of args[] is equal to 1, otherwise returns 0. In addition to the values returned by the function, you can get a signal from the output by reading the passed array out, where the result of the function is stored in the last element of the array.

Not()
Prototype: int Not(usi i1, usi* out);
This function acts as a Boolean element "Not", returns 1 if the argument is 0, otherwise returns 1. In addition to the values returned by the function, you can get a signal from the output by reading the passed array out, where the result of the function is stored in the last element of the array.

Nand()
Prototype: int Nand(usi args [], usi len, usi digits);
This function acts as a logical and-Not element, returns 0 if all args[] elements are equal to 1, otherwise returns 1. In addition to the values returned by the function, you can get a signal from the output by reading the passed array out, where the result of the function is stored in the last element of the array.

Xor()
Prototype: int Xor(usi args [], usi* out);
This function acts as an Exclusive or logical element, returns 1 if one of the args[] elements is 1, otherwise returns 0. In addition to the values returned by the function, you can get a signal from the output by reading the passed array out, where the result of the function is stored in the last element of the array.

Nor()
Prototype: int Nor(usi args [], usi* out);
This function acts as a logical or-Not element, returns 1 if all args[] elements are 0, otherwise returns 0. In addition to the values returned by the function, you can get a signal from the output by reading the passed array out, where the result of the function is stored in the last element of the array.

d_trig()
Prototype: int d_trigg(usi dataIn, usi powerIn, usi digits);
This function implements a D-flip-flop. The data argument is an information pin, the powerIn is the pin that is needed to store the data value in the trigger, digits allows you to select the bit width of the registers in which the output will be saved.

conBuff()
Prototype: int conBuff(usi conSignal, usi mainSignal);
This function implements a controlled diode. The conSignal argument is a control signal. And mainSignal is the main signal. If the control signal is 1 then the output of the diode will be the value of the main signal in the other case at the output 0.

conInv()
Prototype: int CONV(usi conSignal, usi mainSignal);
This function implements a controlled inverter. The conSignal argument is a control signal. And minSignal is the main signal. If conSignal is 1, the inverter output will be the mainsignal inversion.

castElm()
Prototype: int castElm(elm e);
This function returns the value from the output of the elm element passed to it.

customElm43()
Prototype: int customElm43(usi table[4][3], usi i1, usi i2);
This function returns the value from the output of the user element created on the basis of the table of truth passed to it for this element. The arguments i1 and i2 are the inputs of the element. The truth table is 4x3.

Section #2 "Other functions"

setInput()
Prototype: void setInput(usi values [], usi digits);
This function allows you to set the value of Input4 or Input8, the number depends on the value of digits.

SevenSegmentIndicator()
Prototype: void SevenSegmentIndicator(usi pins[]);
This function is intended for data output using
seven-segment indicator.
Segment location and naming:
_	a
|_| ==> b g f
|_| .	c d e p

The function expects the register States of the segments. 8 characters long in the following sequence: {a, b, c, d, e, f, g, p}, such sequences are called IC codes.
Note: it is also advisable to print a dot because it also translates the carriage to a new line.

SSI_SimpleOutput()
Prototype: void SSI_SimpleOutput(char character);
This function takes a symbol which should be output and outputs it.
Available characters are 0-9, A, C, E, F, G, H, J, L, O, P, S, r, U.

button()
Prototype: int button();
This function waits for any key to be pressed when the program starts, as soon as the above event occurs, the function returns 1.

Impulse (in the context of esl.h) is a numeric variable imp which becomes 0 after the operation of any logical element.

impulse()
Prototype: int impulse(usi doIt);
This function changes the value of the imp on the value of doIt.

Result()
Prototype: void Result(usi digits);
This function when run, the program displays the values or Input4 Input8 and Output8 Output4 or.

bus()
Prototype: int bus(usi input [], usi output [], usi lenIn, usi lenOut);
This function implements the bus. I copy the values of the input register to the output register. The lenIn argument is the length of the input, and lenOut is the length of the output. Output length should be greater than or Ravana the length of the input.

transistor()
Prototype: int transistor(double signalCon, double signalMain);
This function implements the transistor. The signalCon argument is the base of the transistor, and signalMain is the emitter.

Section #3 "the Means to operate the registers"

A register (in the context of this documentation) is a one – dimensional numeric array with a given length, taking values of only 1, 0 or en, but IN NO case 14, NEVER!

regInversion()
Prototype: void regInversion(usi reg [], usi len);
This function inverts the values of the reg [] register passed to it.. The value of the len argument is the length of reg[].

regSetValue()
Prototype: void regSetValue(usi reg [], usi values[], usi len);
This function allows you to change the values of the reg [] register to the values of the values [] register. The value of the len argument equal to the length of the register reg[], it is important to note that values[] may not be shorter than the reg[].

regInc()
Prototype: void regInc(usi reg [], usi len);
This function makes all values in reg [] true. The value of len is equal to the length of the reg [] register being transmitted.

regDec()
Prototype: void regDec(usi reg [], usi len);
This function give false all values in the register reg[]. The value of len is equal to the length of the reg [] register being transmitted.

en
This expression indicates the end of the register, so the length of the register is equal to its actual length and +1 for storing en.

Section #4 "Other available tools"
A register (in the context of this documentation) is a one – dimensional numeric array with a specified length that takes only 1, 0, or en values. In esl.h there are built-in registers of 8 elements x2, 16 elements x2, 32 elements x2, 64 elements x2. Built-in functions for working with registers in addition to the built-in ones can perform operations with registers created by you.

Input and output registers-these registers serve built-in functions.
Input4 / Input8 – these registers are intended for input of information as if to set input values for logic elements using these registers, at a call of the Result() function it will be possible to see visually entered and output values from the scheme.
Output4 / Output8 are registers intended for data output, they can be used for a specific method of data output from the scheme.

IC codes
In esl.h starting with version 0.7 available IC codes the following characters:
IC-indicator code (Indicator code)

Symbol	The name of the IC code
0	zero
1	one
2	two
3	tree
4	four
5	five
6	six
7	seven
8	eight
9	nine
A	lettA
B	lettB
C	lettC
E	lettE
F	lettF
G	lettG
H	lettH
J	lettJ
L	lettL
O	lettO
P	lettP
S	two
r	lettR
U	lettU

Analog mode
In esl.h from version 0.12.0 available mode analog representations of data. To use this mode, you must change the analogMode variable from 0 to 1. And for the transmission of analog signals in the Function in which the expected digital data plates function toBool passing it an analog signal it is a Ter digital signal. But the signal should not exceed 15. Also, when working with analog mode, change the limit variable to a value higher than 1 and lower than 0.

Section #5 " Specialized data types"

Strings
General appearance: string <name> = {<"text">, <length>};
Access storke, through the name and str point: <name>.str;
The length of the string is accessed through the name and len through the dot: <name>.size;

Polytypes
General view, initialization takes place in several steps:
1) poly <name>;
2) to_poly(<name>, <value>);
If you want to store a number in <value> this number is specified in quotation marks (""). If you want to access a number stored in a polytype, you can do so using the following syntax: <name>.real_val; if you need the same number but in the form of text, use the following construction: <name>.ch_val;

Elements
General view: elm <name> = {<'type'>, <number of inputs <= 10>, <inputs>};
The number of inputs (10) depends on how much of these inputs across function castElm (not to be confused with customElm).
Example: elm test = {'&', 2, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0};
Here ' & ' means that it is an element And, 2 means that the element has only 2 inputs {'&', 2, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0}, and the rest are not used and filled with zeros. The filling is not used pins with zeros MUST ! If another type of element is required, the following is a list of available symbols:

1. And. ........................................................... '&'
2. OR. ............................................................ '|'
3. NOT. ......................................................... '!'
4. Exclusive - OR (XOR) ................................. '^'
5. Not - And (NAND) ..................................... '~'
6. NOR .......................................................... '#'

usi
usi is short for unsigned short int. Widely used in EHDL_MWE for optimization.

Section #6 " Special operators"

and
General appearance: <operand_1> and <operand_2>
Returns 1 only if both operands are not 0.

or
General appearance: <operand_1> or <operand_2>
Returns 1 only if one or both operands are 1.

not
General appearance: not <operand_1>
Returns 1 only if the operand is 0.

xor
General appearance: <operand_1> xor <operand_2>
Returns 1 only if both operands are not equal to 1 and both operands are not equal to 0.

shir
From (shift right), General view: <operand_1> shir <operand_2>
Shifts <operand_1> by <operand_2 > bits to the right.

shil
From (shift left), General view: <operand_1> shil <operand_2>
Shifts <operand_1> by <operand_2 > bits to the left.

$()
General appearance: <operand_1> $(<operand_2>)
Increases <operand_1> <operand_2>.

_()
General appearance: <operand_1> _(<operand_2>)
Reduce <operand_1> <operand_2>.

Section #7 " error Types"

In EHDL since version 0.11.1 the additional system of search of errors is entered. At this point, you may encounter only two types of errors.

Type 1. This error code-named BTE (Bool Type Error), the error occurs when you try to transfer the analog value to where expected digital.

Type 2. These are errors codenamed PVE (Polytype Value Error), they occur when interacting with the polytype it turns out that the values of the polytype fields are different when reduced to numbers.

Standard debugger EHDL_MWE
Documentation for the esd header file.h version 1.0 and above.

Section #1 " Debugger"

go()
Prototype: void go(int block1, int block2, int block3, int block4);
This function runs the code block defined by the arguments. If blockn is not set to 0, this block will be executed.

part1 () / part2 () / part3 () / part4()
Prototypes: void partner (); (n is a number, 1 <= n <= 4)
These functions are blocks of code executed by go(). All blocks used must be defined.

Additional native library file EHDL_MWE ael.h
Documentation.

summator()
Prototype: void summator(usi p, usi a, usi b, usi* s, usi* pi);
This function implements the adder.

halfadder()
Prototype: void halfadder(usi x, usi y, usi* s, usi* c);
This function implements a half-accumulator.

major()
Prototype: void major(x1 usi, usi x2, x3, usi, usi* y);
This function implements the majority element.